## Slide 1: Observing Tool (updated to ALMA Cycle 5)
E. Liuzzo
credits to Kazi Rygl, A. Giannetti, M. Massardi
Italian ARC node, IRA-BO

## Slide 2: Observing Tool (OT) for ALMA Cycle 5
java-based tool retrievable from almascience website
  webstart version (always updated)
  tarball version (offline working, might be outdated)
the only way to submit your ALMA proposal
the OT offers a visualization of spatial setting (e.g., pointings in a mosaic), spectral settings (correlator tuning), time estimator, sensitivity calculator, and messages when settings incompatible

## Slide 3: Starting up the OT
PI/CoI have to registered on almascience website
select proposal type (regular, VLBI, ToO, large program)
select scientific category
if resubmission of previous Cycle, enter the project ID
if resubmitting an already submitted Cycle 5 project, make sure that you it contains the project ID on the Project Tab to avoid duplication

## Slide 4: OT graphical interface

## Slide 5: Science Goals
For sources distributed widely in the sky the SG will be split by the OT into different “clusters”.
Each grouping all sources within 10 degrees.
No restriction on the total number of sources in a SG, but for each grouping within the SG, the total number of pointings must be less than or equal to 150.
Max 5 tunings per given group of sources (spectral scan)

## Slide 6: Field setup
Resolve by Source Name (NED, Simbad)
SSO incl. Sun (tick box, select object, Sun, Ephemeris: upload ephemeris file)
upload Sources from file (see help for file format)
✒︎important: expected source properties

## Slide 7: Spectral setup
Continuum (single, dual, full pol)
Spectral line (single, dual, full pol)
Spectral scan (single, dual pol)
4 basebands (BBs), each max 2GHz, to be placed in two sidebands
widths SB different per band (band 3,4,5,7,8: 4GHz; band 6: 5GHz; band 9,10: 8 GHz)
carefully select the representative spw: will be used for all frequency/spectral resolution dependent calculations, such as FOV, MRS, angular resolution, atmospheric opacity

## Slide 8: Spectral setup
Continuum (single, dual, full pol)
Spectral line (single, dual, full pol)
Spectral scan (single, dual pol)
Band 5 is now offered
- be careful H2O atmospheric line
- only available from March 2018 (no warning from the OT)
90-degree Walsh switching Band 9 and 10
-16 GHz instantaneous bandwidth could be available with some spectral setup
define rest frequencies of lines
-information is used for QA2
New!!

## Slide 9: Spectral line setups
Use the ALMA spectral line database
Continuum BB and spectral line can be mixed (Spectral line mode)
Set unused spws to continuum to help with calibration and continuum removal, in particular if you have narrowband spw
sidebands
basebands
2 spw in
one baseband
in each BB can contain up to 4 spectral windows (spw)
all spws in one BB should have the same resolutions
better higher spectral resolution, but keep data rate < 40MB/s — the default correlator setup for FDM modes averages every two channels
New!!

## Slide 10: Baseband limitations
Bad spectral configuration
BBs stay gray in spectral viewer
Spectral configuration OK
BBs become yellow
2SB receivers (bands 3,4,5,6,7,8) cannot have 3 BBs in one sideband and 1BB in the other
DSB receivers (bands 9,10) have no BB/sideband restrictions
Band 6
Band 6
Bad spectral configuration gives error messages in red

## Slide 11: Spatial setup, once the spectral setup is done
text
Primary beam or FOV ~ λ/D
Repr. freq from spectral setup
Rectangular field (mosaic)
Individual pointing
(cannot contain multiple offsets)
clone source for multiple offsets
New!!

## Slide 12: Control and performance
OT calculates the angular resolution/maximum recoverable scale (MRS) for the most extended and most compact 12m Array, and the ACA 7m array based on the frequency and the source declination
Based on the user selected resolution and MRS the OT will choose the most suitable array(s) (incl. ACA stand alone)
OT Time estimation uses the sensitivity calculator to derive the total time for the SG incl. calibration. It will divide sources with large separations in clusters that have their own calibrators, and show the number of tunings per cluster.
Enter the desired performance, angular resolution, MRS, sensitivity and the bandwidth for sensitivity

## Slide 13: Control and performance
Angular resolution interface is more flexible
- single/ range/ any / Standalone ACA
- possible configurations are given
New!!

## Slide 14: Other for Cycle 5
Calibration Setup more flexible, but it will be a non-standard mode
Time constrained observing more flexible
Resubmissions now flagged by the observatory, duplications must be justified
Full polarization available in all low-frequency bands (Bands 3-7)
Overlaid lines are saved
New!!

## Slide 15: Technical Justification
Justify your chosen sensitivity and bandwidth for sensitivity✍
OT gives a sensitivity summary: requested and achieved RMS and S/N in req. bandwidth
Spectral observations: OT gives S/N over 1/3 of the linewidth, and linewidth/bandwidth for sensitivity ratio, gives also the spectral dynamic range
Justify your angular resolution and MRS✍
OT repeats the angular resolution and MRS
Justify your spectral resolution and data rate✍
OT repeats linewidth/spectral resolution of representative spw, and gives bandwdith of representative spw

## Slide 16: Technical Justification
Justify your chosen sensitivity and bandwidth for sensitivity✍
Justify your angular resolution and MRS✍
Justify your spectral resolution and data rate✍
Numbers to be double checked trigger a message in blue
Figures/Tables required for Technical Justification have to be present in Scientific Justification
Only spectral dynamic range < 1000 (B3,4,6) /500 (B7,8,9,10) allowed
Check the knowledgebase
if you encounter problems or contact us!

## Slide 17: Completing the proposal
1. Validate your proposal
This brings up any problem, such missing Scientific Justification, or badly set spectral settings.
Only validated proposal can be submitted!
2. Display project time summary
Gives an overview of observing time of all proposal and the data rate plus expected data size
3. Make a pdf overview and save the .aot file on your disk
Validation errors are given in the Feedback window

## Slide 18: OT documentation and Help
OT Help includes the User manual and reference guide
ALMA website contains the OT quickstart guide, manual and reference guide, proposers guide, and OT video tutorials
OT contains the ALMA template library of aot files
Submit questions to the ALMA Helpdesk or your ARC!

## Slide 19: Limitations for Solar and VLBI proposals
Solar observations: continuum mode (single or dual pol) in a predefined spectral range of band 3 and 6.
VLBI observations: continuum mode (full pol) in a predefined spectral range of band 3 and 6, and require a separate proposal to the GMVA or EHT
PI does not ask for a sensitivity,
but directly for observing time in limited time slots